## Slide 1: A 3DIC system to aid in the acceleration of systems that employ multiple instances of artificial neural networks
Status Apr 2017
Lee B. Baker
Advisor: Paul Franzon
Notes: I suspect most of us have seen reports on self-driving cars.
But how can a car determine whats in its surroundings?
One piece of technology that is and will be used is Artificial neural networks
These artificial neural networks allow the vehicle to recognize street signs, other vehicles, pedestrians, edges of the road, all the things you might need to safely navigate a 2-ton car.
The ability for artificial neural networks to perform that function in a timely fashion within reasonable power and space constraints is what I am going to talk about today.

## Slide 2: Introduction
Recently Artificial Neural networks (NN) have demonstrated superior performance in classification and function approximation
  Deep Neural Networks (DNN) have been very successful in image processing applications [Kri12]
  it is anticipated that DNNs will be employed more and more in self-driving cars
  Reinforcement learning is gaining popularity
  alphaGo employed reinforcement learning with deep neural networks [Mad14]
http://www.hackerboards.com
http://www.BGR.com
http://www.engadget.com
Notes: Now I mentioned self driving cars,
but recently ANN’s have also demonstrated efficacy when employed as a part of face recognition, text recognition and game playing systems
These ANN’s have demonstrated significant improvements over current state of the art.
Some example uses of ANN’s are the google car and you may also have recently seen the Go game system AlphaGo, which recently “beat” a Go master.
So ANN’s are being deployed as we speak and we should therefore consider them to be in the ascent phase of the technology life cycle.

## Slide 3: Introduction
Many applications will and do require multiple NN engines running at or near real-time
  car or drone scanning in many directions during navigation
  cloud server processing multiple images when searching
  reinforcement learning requires multiple state-action value calculations during optimal policy searches
  text recognition system processing multiple pages of text
Notes: Many applications require information to be provided at or near real time or simply have large volumes of data to process.
This means these systems will require multiple ANN’s to be running concurrently
A vehicle will need real time feedback on its surroundings.
A cloud server performing text or image searches must provide feedback in seconds.
Text recognition may not have a real-time requirement but just the volume of work requires we process in parallel
to complete the work in a reasonable time

## Slide 4: Problem
Many applications will/do have power, space and weight limitations
  drone
  server rack has building cooling limitations
Useful Neural Networks are big
  lots of memory and computations  bandwidth
  local SRAM consumes too much silicon
  locally and fully connected networks are bandwidth limited
To achieve near or at real-time processing, current solutions require high power and high real-estate
  GPU solutions have large real-estate and power requirements (~100-200W)
  ASIC’s target smaller network sizes and/or specific NN’s
  ASIC’s often employ SRAM which consumes a high percentage of silicon
  Both have memory bandwidth limitations
Notes: The problem is having a system implement multiple of these ANN’s in real time.
Effective ANN’s are big, they contains lots of neurons.
Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements when supporting useful NN’s (GPU ~100W)
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 5: Solution
3DIC Architecture
  reduces energy and area
  increase connectivity and bandwidth
3D-DRAM
  provide high bandwidth and large storage
  minimize dependency on SRAM to allow available silicon to be focused on processing
  eliminate NN size restrictions imposed by local SRAM
Data Structures
  data structures to ensure neural network data can be accessed efficiently from primary storage (DRAM)
  maintain constant access to DRAM to avoid dependency on local SRAM
Specialized processing layers
  provide special functions to aid in acceleration of target neural networks
  avoid local memory imposing NN size limitations
  focus available silicon on processing requirements
http://www.semiwiki.com
Notes: This work proposes taking advantage of 3D IC technology.
This 3D architecture will include a custom organized 3D DRAM to store the neural network and Data structures designed to access that DRAM effectively.
The proposal also includes custom processing layers to perform the NN computations.
Using DRAM addresses the large network size requirement
and the 3D architecture ensures we can address bandwidth, space and power issues.
The custom processing layers will be targeted toward a family of ANN’s

## Slide 6: Contribution
Research uniquely organized 3DIC DRAM
  research bank and page organization for a family of neural networks
  maintain efficient read and writing
Research and propose Data Structures to exploit DRAM capacity
  in conjunction with DRAM organization
  data structures organized to allow efficient streaming of data directly to processing layers
  employ data duplication
Propose 3D architecture to take advantage of DRAM bandwidth
  memory management to manage configuration and algorithm operations and coalesced accesses
  processing layer contains special functions for a family of NN’s
Notes: The primary contributions of this work is
- a custom organized 3DIC DRAM allowing us to provide the necessary memory bandwidth to process multiple ANN’s in real time
- data structures for storing parameters and neuron activation values
- a 3D architecture which will ensure the bandwidth provided by the custom memory can be processed at line rate by a processing layer customized to the functions required to process the target ANN’s
Combining these contributions will allow us to demonstrate a significant performance improvement overcurrent solutions

## Slide 7: Outline
What are artificial Neural networks
Target Neural networks
State-of-the-art
Proposed Architecture
  Problem
  Solution
Preliminary Work
  3DIC DRAM and data structures
  3D Stack Bus
  Processing Layer
Research Plan
Summary

## Slide 8: Target ANN Type’s
This work will focus on the following ANNs :
  Deep Neural Network Classifiers
  ANN in Reinforcement Learning
  Cogent Confabulation
  Brain-state-in-a-Box
Our research will involve analyzing memory access and processing requirements
Notes: DNN classifiers because of their performance in image recognition
ANN in reinforcement learning because of their use as value function approximator
and finally Cogent Confabulation and BsB because of their joint efficacy in a text recognition system

## Slide 9: Outline
What are artificial Neural networks
Target Neural networks
State-of-the-art
Proposed Architecture
  Problem
  Solution
Preliminary Work
  3DIC DRAM and data structures
  3D Stack Bus
  Processing Layer
Research Plan
Summary

## Slide 10: Problem
System solution requiring multiple NN’s
  Consider a system that requires ~8 DNNs[Boj16]
  ~16Gb of memory
  ~100W per GPU suggests >800W total power
Real-Time
  Image needs to be processed ~16mS (60 frames/sec)
  Allowing ~10mS for classification requires ~1700GFLOPS1
  Required Memory bandwidth ~54Tbps
Current 3D-DRAM memory technology bandwidth
  HMC – SERDES~2Tbps
  HBM – wide DDR ~2Tbps
  Tezzaron DiRAM4 – wide DDR – 4Tbps

## Slide 11: Solution
Utilize DRAM as the primary processing memory
  allows support of locally and fully connected NNs
  improves NN size support with near deterministic performance
  not optimal for NNs that take advantage of locality
Processing Layer can be customized
  PE layer designed to support application specific accuracy, algorithm etc.

## Slide 12: Solution
Architecture includes:
  Custom organized 3D-DRAM specification
    allows constant streaming of data to PE avoiding local storage
  Data Structures specific to each ANN
  Management Layer for configuration and control
  Processing layer(s) targeted toward a family of ANNs
    array of processing engines (PE) with special streaming functions
    PE includes small SIMD unit to process non hot-spot functions and provide some generality
3D solution contained within the footprint of available DRAM
  allows use of TSV’s for memory interface
  PE provides 32 execution lanes within the footprint
  minimal use of local SRAM allows PE and manager logic to fit within footprint
Notes:     Mention multiported
    Memory layers, control layer and processing layer could use different technology
    SSF’s will operate directly on data read from stack bus
    To increase bus widths, increase bandwidth while minimizing interface power
provide access to entire page rather than cache-line
there will be power considerations by not taking advantage of some reuse of data in local memory but I believe the performance benefits will outweigh the disadvantages
    Special streaming functions will also have the ability to operate on data in processing layers expected small amount of local memory
    avoid DRAM page open latency by using a highly banked DRAM and arranging data in memory to allow back-to-back page opens
    Careful consideration of layer state and kernel parameters required to maximize DRAM bandwidth

## Slide 13: Solution Block Diagram
Total downstream B/W
131Tbps
Array of processing engines
(PE)
Custom organized DRAM
Management Layer

## Slide 14: Potential Customers
Google current have their own solution in the datacenter space
  Tensor processing unit is a custom ASIC
    large local SRAM and a large array (64K) of 8-bit MACs
    lower DRAM bandwidth
  High percentage of their NNs are MLP and LSTM and smaller percentage (5%) are CNNs
    CNNs take advantage of locality and are suited to using large local SRAM
    it may be the case that as MLP and LSTM have many fully/locally connected layers, they are impacted by a low main memory bandwidth
3D DRAM System could provide performance improvement in accelerating MLPs and LSTM
  provide the bandwidth to support the bulk of the NNs processed in their datacenters
  a custom 3D solution could provide a PE layer to support the target resolution
    perhaps work with google to integrate 8/16-bit PE similar to their TPU

## Slide 15: 3D Configuration
Array of processing engines
(PE)
Custom organized DRAM
Management
Layer

## Slide 16: System Column
Each column includes:
  port into 3D-DRAM
  Manager for configuration, DRAM reading, writing and data duplication
  PE
Idea is to read and write mainly from DRAM
  no assumptions on data reuse (kernels or input)
  input or weight reuse would be more optimal but we are providing a more flexible high bandwidth solution
Solution includes instructions to describe operations required for a group of neurons
  operations performed by PE
    PE operates on two streams from manager e.g. weight/input
  where input and weights reside in DRAM
  where to write results including duplication to other columns
Notes:     1.7 102 OPS
    assume 1GHz
    1700 OP/cycle => 2048 execution units
    each of the 64 ports needs to support 32 execution lanes
Note:
Initial discussion with 3D-DRAM supplier suggests idea is achievable

## Slide 17: System Column
A processing column includes:
  DRAM port
  Manager
    process set of instructions which implement a NN
    manage configuration of PE and communication of results
  PE
    take data from Manager/DRAM via stack bus
    operate on data at line rate to generate neuron activations
    silicon focused on processing required not storage

## Slide 18: Instruction Format
Instruction must describe operations for processing a group of neurons
  convolution of weights and input
  Relu or Sigmoid to generate activation
  where and how to read weights
  where and how to read prior activations
  where and how to save neuron activations
Instruction formed from four descriptors
  PE operation
  Weight read operation
  Input read operation
  Write-Back operation
Instruction decoder generates control messages from descriptors:
  Operation descriptors sent via OOB configuration packets to PE to configure SIMD and stOp
  Write descriptor sent to a Return Data processor describing where result from PE should be sent
  Read descriptors sent to memory modules to stream data to PE

## Slide 19: Instruction
Includes four descriptors
  operation
  memory read (2)
  result write

## Slide 20
Instruction Format
Instructions formed from a set of descriptors
Descriptors for:
  Operations
  memory Read
  memory Write
  access method
Operation descriptor
  defines SIMD and stOp operations
  SIMD and StOp operation stored in PE instruction memory
  descriptors point to instructions in PE IM
Memory read and write Descriptor
  sets start address
  describes how address is accessed
    bank/page/word increment order
    how data is transferred to stack bus and on to PE
  memory descriptor points to an access descriptor that is stored in manager memory
  expect commonality amongst access methods so many descriptors may point to same access descriptor
Access descriptor
  not used in the actual instruction
  expect some commonality between memory read and writes so avoid replicating access descriptor

## Slide 21: 3D Stack Bus

## Slide 22: Stack Bus
Each processing column has a downstream and upstream stack bus
  Downstream 20481 bit running at 1GHz providing131Tbps raw system bandwidth
  Upstream bus 5122 bits running at 1GHz
    result bandwidth ~1/100th of operand bandwidth

## Slide 23: Stack Bus
Downstrean and upstream buses
Buses carry control packets and data packets
  packets will be multiple clock cycles
Control packets used to configure PE
  special function and SIMD operations
  result information
Data Packets will carry arguments for special functions
  data to will be multiple cycles of two 32-bit words
Notes:   result information such as unicast or multicast, destination page
Return bus can be driven by all layers
  research will determine if bus is arbitrated or whether each layer buffers and forwards

## Slide 24: Processing Layer

## Slide 25: Special Functions in PE
Special Functions are designed to operate on data from the Stack bus
  operate at line rate from downstream bus
  perform computations directly as data is read from memory
  avoid need for large local SRAM in PE
  result is passed to “small” local memory or registers for later processing by SIMD
  result sent to upstream bus
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 26: PE Status
FMA streaming operation functionality coded
SIMD has yet to be integrated
  a wrapper around SIMD allows system to operate normally except SIMD doesn’t process neuron outputs
SV environment generates PE configuration packets and streams neuron weights and inputs to PE
  Result verified by examining result packet on upstream stack bus

## Slide 27: Management Layer

## Slide 28: Manager
Ensure data can be streamed efficiently from DRAM
Operates on a custom instruction set
  instructions describe all that is necessary to process a group of neurons
  avoid need for large local SRAM in PE
System requires data duplication
  NoC designed to multicast neuron activations to other managers
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 29: Manager Status
Basic functionality except Memory read and Write are coded
Manager instructions generated from python script
  instructions include a group of descriptors that specify:
    PE operation
    source of weights and inputs
    where to write results
  python script generates readmem files
SV
  environment still generates neuron weights and inputs to PE
  Manager code generates configuration packets from instructions
  Manager code takes results from upstream stack bus and constructs NoC packets for writes to local memory and other manager memory

## Slide 30: Verification Block diagram

## Slide 31: Instruction Communication

## Slide 32: NoC Signaling