## Slide 1: A 3DIC system to aid in the acceleration of systems that employ multiple instances of artificial neural networks
Final exam : Lee B. Baker
Advisor: Paul Franzon
Notes: I suspect most of us have seen reports on self-driving cars.
But how can a car determine whats in its surroundings?
One piece of technology that is and will be used is Artificial neural networks
These artificial neural networks allow the vehicle to recognize street signs, other vehicles, pedestrians, edges of the road, all the things you might need to safely navigate a car
The ability for artificial neural networks to perform that function in a timely fashion within reasonable power and space constraints is what I am going to talk about today.
We are going to review a system that is able to accelerate multiple instances of disparate useful sized artificial neural networks and provide power and/or area benefits over current state-of-the-art

## Slide 2: Introduction
Recently Artificial Neural networks (NN) have demonstrated superior performance in classification and function approximation
  Deep Neural Networks (DNN) have been very successful in image processing applications [Kri12]
  it is anticipated that DNNs will be employed more and more in self-driving cars
  Reinforcement learning is gaining popularity
  alphaGo employed reinforcement learning with deep neural networks [Mad14]
http://www.hackerboards.com
http://www.BGR.com
http://www.engadget.com
Notes: Recently ANN’s have demonstrated efficacy when employed as a part of face recognition, text recognition and game playing systems
These ANN’s have demonstrated significant improvements over current state of the art.
Some example uses of ANN’s are in car navigation, likely the google car and you may also have recently seen the Go game system AlphaGo, which recently “beat” a Go master.
So ANN’s are being deployed as we speak and we should therefore consider them to be in the ascent phase of the technology life cycle.

## Slide 3: Introduction
What about applications that will and do require multiple NN processors running at or near real-time?
  drone scanning in many directions during navigation
    looking down different than looking forward??
  aircraft performing system diagnostics during flight
    observing thermal profiles
    observing vibrations
  airport security
    face recognition
    body thermal profiles
    motion
Notes: Its this works assumption that many embedded applications will require these ANNs to be processed at or near real time.
This means these systems will require multiple ANN’s to be running concurrently
A vehicle will need real time feedback on its surroundings or monitoring its own systems
airport security

## Slide 4: Introduction
Most useful ANNs are big
  100’s of thousands of artificial neurons
  real-time processing requires lots of memory bandwidth and storage
Notes: Most ANNs are big and the trend is that ANNs are becoming larger and deeper
There is general acceptance that DRAM needs to be used to stored the parameters associated with an ANN
But many implementations have focused on using SRAM as an intermediate store.
This has proved to be very effective when there are reuse opportunities where these cache-like structures can be accessed multiple times and thus keeping the slower DRAM accesses to a minimum.
But these implementations rely on reuse.
The main reuse opportunities come in the form of shared parameters and batch processing.
other types of ANN such as DNN with non-shared kernels and LSTM are exposing limitations of these current implementations

## Slide 5: Research
Most research focused on CNNs
  can take advantage of SRAM using parameter reuse
A lot of focus on server applications
  perhaps lots of research $$ available??
  server applications can take advantage of SRAM for batch processing
But many DNNs are fully-connected [XX]
  LSTM and MLPs
  classifier stage of all ANNs including CNN
Notes: The problem is having a system implement multiple of these ANN’s in real time.
Effective ANN’s are big, they contains lots of neurons.
Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements when supporting useful NN’s (GPU ~100W)
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 6: Mission Statement
Real world applications will require multiple disparate NNs to be solved simultaneously
  If ANNs fulfill their potential, we believe that systems employing ANNs will utilize them for various functions, such as engine monitoring, anomaly detection, navigation etc. all within the same system
We need the capacity provided by Dynamic Random Access Memory (DRAM)
  SRAM is easy to use, but capacity limitations impose ANN size restrictions. DRAMs are difficult to use but they provide the capacity we need.
  Much of the research has employed SRAM. Perhaps because it provides high bandwidth but could it also be because its easy to use
  Some research has employed DRAM, but its often used as a feeder to an SRAM based implementation.
Need to consider the system impact
  Research often focuses on point problems. This isn't unreasonable, research institutions have limited resources.
Notes: During the creation of this works system, when I had the urge to add SRAM because it made things easier, I forced myself to think how I could solve it with just the DRAM
This work is proposing using 3DIC technology, and in this case I felt it was important to also get a very good feel for the area associated with such a system

## Slide 7: Problem
Many embedded applications will/do have power, space and weight limitations
  to achieve near or at real-time processing, current solutions require high power and high real-estate
    GPU solutions have large real-estate and power requirements (~100-200W)
    ASIC’s demonstrate significant improvements over GPUs
    Most have memory bandwidth limitations when reuse opportunities do not exist
  multiple disparate ANNs means limited reuse opportunities and thus SRAM is of limited use
  no or limited batch processing
Notes: The problem is having a system implement multiple of these ANN’s in real time.
Effective ANN’s are big, they contains lots of neurons.
Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements when supporting useful NN’s (GPU ~100W)
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 8: Solution
3DIC Architecture
  reduces energy and area
  increase connectivity and bandwidth
3D-DRAM
  provide high bandwidth and large storage
  operate directly out of DRAM
Data Structures
  data structures to ensure neural network data can be accessed efficiency
Specialized processing layers
  provide special functions to aid in acceleration of target neural networks
Notes: This work proposes taking advantage of 3D IC technology.
This 3D architecture will include a custom organized 3D DRAM to store the neural network and Data structures designed to access that DRAM effectively.
The proposal also includes custom processing layers to perform the NN computations.
Using DRAM addresses the large network size requirement
and the 3D architecture ensures we can address bandwidth, space and power issues.
The custom processing layers will be targeted toward a family of ANN’s

## Slide 9: Solution
Can a 3D-DRAM be used effectively?
Can a useful system fit within the 3D stack?
How can we control such a system?
Notes: The primary contributions of this work is
- a custom organized 3DIC DRAM allowing us to provide the necessary memory bandwidth to process multiple ANN’s in real time
- data structures for storing parameters and neuron activation values
- a 3D architecture which will ensure the bandwidth provided by the custom memory can be processed at line rate by a processing layer customized to the functions required to process the target ANN’s
Combining these contributions will allow us to demonstrate a significant performance improvement overcurrent solutions

## Slide 10: Contribution
An extensible architecture that can simultaneously process multiple disparate real-time DNNs
  with low power and real estate demands
Proposed a custom 3D-DRAM providing a ~32X bandwidth benefit compared to standard 3D-DRAM
  wider bus and expose more of the page
A DNN system solution that employs pure 3DIC technology
  providing power and performance benefits of remaining within a 3DIC stack
Custom instructions and data structures that facilitate operating directly out of 3D-DRAM
  provide the required processing bandwidth by ensuring effective use of the 3D-DRAM
  instruction format allow system functions to operate concurrently

## Slide 11: Outline
What are artificial Neural networks
Target application and ANN type’s
State-of-the-art
System Architecture
  Problem
  Solution
System details
  3DIC DRAM and data structures
  3D Bus
  Manager
  Processing engine
Results
Summary

## Slide 12: Artificial Neural Networks
a network of processing elements inspired by the connectivity and processing observed in the brain
the processing elements or neurons are connected together to form a network
Notes: Neural networks are a mathematical model, but they are advertised as being inspired by neurons in the brain.
Mention this is the basic neuron model used is almost all ANN’s
Mention it has been well understood that when organized like this a network of ANN’s can be used to solve complex functions and classifiers
The terminology used is the neuron being considered is the post synaptic neuron when they are linear function approximators

## Slide 13: Artificial Neural Networks
the processing elements fall into two categories
  rate based neurons which try to capture the neuron behavior in the form of a number
    relatively simple to model
    information stored in the form of strength of connections
    easier to train and have shown high levels of efficacy in many applications
  spiking neurons which more closely emulate actual brain behavior
    model neural activity in the form of differential equations
    require numerical methods to solve although there have been attempts to employ analog circuits
    information stored in the form of strength and delay of connections
    complex and hard to train
In this work we are focusing on rate based ANNs
Notes: Keep this concise
Real neurons generate spikes
Believed that information is carried in spike rates
Rate coding is a simplification
    Rate-based neural network used when we see demonstrations from google etc.
Spiking considered more powerful

## Slide 14: Artificial Neural Networks Rate-based
Information stored in connection weights
Output of network is class probability or a value
Output of neuron is fixed value
Multiple layers of neurons
Outputs of each layer feeds next layer
Notes: Keep concise
Mention ReLu function

## Slide 15: Artificial Neural Networks Rate-based

## Slide 16: Summary : Target application and ANN type’s
Embedded systems
  not cloud based
  assumes multiple tasks are being performed
  requires multiple disparate ANNs
This work has focused on the DNNs :
  Classifiers
  function approximators
  CNNs and DNNs
  can be extended to support LSTMs
Notes: DNN classifiers because of their performance in image recognition
ANN in reinforcement learning because of their use as value function approximator
and finally Cogent Confabulation and BsB because of their joint efficacy in a text recognition system

## Slide 17: Deep Neural Network Classifiers
Currently the most popular ANN
  trained offline
  Convolutional NN’s have been very successful in classification
  locally-connected NN’s also used in face recognition
  fully-connected includes LSTM
This work focuses on inference in embedded applications
Notes: Trained offline
Used for inference
Deep Neural Networks (DNNs) are feed-forward multi-layered neural networks
Each layer identifies features in the previous layer
  Features are identified by convolving a filter (kernel) over a Region of Interest (ROI) in the input
  CNNs are a class of DNNs that use the same feature kernel across the entire input layer(s)
Layers separated using a non-linearity (tanh, sigmoid, ReLu)
  ReLu is becoming a popular choice
Final layers are typically fully connected classifiers
  in classifiers outputs are one-hot softmax probability
    each output represents a class such as Tank, cannon, house, pickup truck, dog, hoagie
  in function approximator each output represents a value
    in reinforcement learning, the value represents an action reward

## Slide 18: State-of-the-art
Current implementations either use GPU’s or low capacity ASIC implementations
GPU’s are typically general purpose devices and consume high power
  GPU’s do lend themselves to convolution when weights are shared
  ASICs almost always provide performance iprovements
ASIC implementations target larger networks by using multiple devices
  usually assume local SRAM which limits network size
  some/most implementations target specific NN’s, usually CNNs

## Slide 19: State of the Art
ASICs
  Most employ arrays of processors
  Some target specific ANNs
  Most cannot support useful sized NNs with single device
  Many process data from local SRAM memory which often consumes >60% of silicon area
  demonstrate performance improvements over GPUs

## Slide 20: State of the Art ASIC’s
ASIC’s
Eyeriss[Che16]
NeuroCube[Kim16]

## Slide 21: State of the Art ASIC’s
NeuroCube1
  uses HMC 3D-DRAM but dependence on SRAM limits support to CNNs
Eyeriss2
  discusses DRAM accesses but their focus is on the convolution operation
  supports CNN convolution operation only
NnSP3
  uses cache between DRAM and 8Mb SRAM and will be limited by DRAM bandwidth
  does not discuss multi-devices
Neuflow4
  limits their support to CNNs and in the case of Eyeriss only supports the convolution
  will not support locally-connected ANNs
Notes: What measure would you use?

## Slide 22: More recent State of the Art ASIC’s
NeuroStream
  acknowledges DRAM is required for useful DNNs
  uses HBM 3D-DRAM along with local SRAM
  depends on SRAM for performance
Google TPU
  assumes large levels of batch processing
  8-bit processing
  fully-connected NNs represent very high percentage
  acknowledges performance degradation using fully-connected
DaDiannao
  uses embedded DRAM but still requires up to 64 for useful DNNs
  high internal bandwidth but dissipates high power when scaling to useful-sized ANNs
Notes: What measure would you use?

## Slide 23: State of the Art GPU’s
GPU’s target the general market and employ infrastructures not necessary for NN implementation
  we associate power of GPU solution ~100-200W
  Will still be limited by memory bandwidth although they are starting to utilize 3D-DRAM
  general purpose architecture makes it hard/impossible to make full use of theoretical performance
[Far11]

## Slide 24: State of the Art
Current state-of-the art ASIC’s and GPU’s do not provide the capacity and efficiency to provide a solution requiring multiple useful disparate ANN’s to be computed in real-time

## Slide 25: Problem
System solution requiring multiple NN’s
  ~8GB of memory
  real-time processing : ~16mS (60 frames/sec)
  ~26Tbps memory bandwidth
Current 3D-DRAM memory technology bandwidth
  HMC – SERDES~2Tbps
  HBM – wide DDR ~2Tbps
  Tezzaron DiRAM4 – wide DDR – 4Tbps
Goldilocks principle
  need balance of bandwidth and storage
  currently bandwidth too low

## Slide 26: Solution
Architecture includes:
  Custom organized 3D-DRAM specification
  Data Structures specific to each ANN
  Management Layer for configuration and control
  Processing layer(s) targeted toward a family of ANNs
  array of processing engines (PE) with streaming functions
    multiply/accumulates ANe activation
    multiply for softmax
  additional special functions used in the neuron activation process
    ReLu for ANe activation
    divide and exponent for softmax function
    compare for pooling
Notes:     Mention multiported
    Memory layers, control layer and processing layer could use different technology
    SSF’s will operate directly on data read from stack bus
    To increase bus widths, increase bandwidth while minimizing interface power
provide access to entire page rather than cache-line
there will be power considerations by not taking advantage of some reuse of data in local memory but I believe the performance benefits will outweigh the disadvantages
    Special streaming functions will also have the ability to operate on data in processing layers expected small amount of local memory
    avoid DRAM page open latency by using a highly banked DRAM and arranging data in memory to allow back-to-back page opens
    Careful consideration of layer state and kernel parameters required to maximize DRAM bandwidth

## Slide 27: Solution
3D-DRAM is the Tezzaron DiRAM4
  64 disjoint 1Gb memory ports
  System has 64 sub-systems each operating on one memory port
Suggested Customizations for a 3D-DRAM
  Standard DiRAM4 port is 32bits @ 1GHz
  We suggest widen to 2048 bits and use high-density TSVs
  Entire page in one access using burst-of-2
  Raw bandwidth ~2Tbps per port

## Slide 28: Solution
System has 64 sub-systems each operating on one memory port
  ANNs split over sub-systems
Sub-system has a Manager and PE
  Data-path between DRAM, Manager and PE
    data for 32 execution lanes with two arguments per lane
    able to perform a MAC operation between a weight and ANe state every cycle
    process a group of 32 ANes each instruction
  Result path from PE to Manager
    carries result(s) of processing a group of ANes
    return data contains up to 32 words
  Instruction Decode in Manager
    contains information on how to process a group of Anes
    where are weights, ANe states and result stored

## Slide 29: Solution Block Diagram
Total downstream B/W
64Tbps
Array of processing engines
(PE)
Custom organized DRAM
Management Layer

## Slide 30: 3D Physical Configuration
Array of processing engines
(PE)
Custom organized DRAM
Management
Layer

## Slide 31: Sub-System Column (SSC)
Consists of DRAM, manager and processing engine (PE)
logical
physical

## Slide 32: 3D Stack Bus

## Slide 33: System
Need to absorb DRAM latency
  separate memory requests from read/write data
Instruction spawns multiple commands to dependent tasks
  concurrently pre-fetch data, prepare PE, prepare Return Data Processor
  all operations have an associated tag
Need to describe parameter and state storage
  assume input stored in row-major fashion
Network-on-Chip
  needed for ANe state replication to all dependent SSCs

## Slide 34: Instructions
Instructions consist of descriptors
Descriptors used to control modules which take part in the instruction
Descriptors contain tuples which contain the details

## Slide 35: Data Storage and access
Inputs and ANe states stored in row-major
Weights for a group of ANes are interleaved

## Slide 36: Manager Layer
Decodes instructions
  sub-descriptors are sent to dependent blocks
Reads and writes to main memory
Communicates to host and other SSCs
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 37: Processing (PE) Layer
Streaming operations operate on data directly from the Stack bus
  MAC, Multiply
SIMD Wrapper performs post stOp tasks
  add/divide/exponent, sends result back to manager
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 38: AREA
Area based on DiRAM4
  SSC needs to fit into footprint of DiRAM4 sub-memory
  available area is 2.43 sq-mm

## Slide 39: AREA
Scaling based on synthesizing representative block at 28nm and 65nm
Manager/PE Block sizes

## Slide 40: Area placement study
Placed and routed without DRC or LVS
Routing congestion showed minimal hotspots
Parasitics used in Primetime for power analysis

## Slide 41: Power Summary
Power estimates based on CONV-294 testcase simulation
  back to back operations
  accumulate DRAM access and use DiRAM4 datasheet [xx]
  TSV energy from [XX]
  parasitics from layout
  designed using 65nm library
  28nm is target technology
  power and area scaling based on synthesizing representative blocks

## Slide 42: Research
Specify a custom organization of a 3DIC DRAM
  provide a specification showing memory organization, bus widths
Create Structures/Instructions to exploit DRAM capacity
Propose 3D architecture to take advantage of DRAM capacity and bandwidth
  RTL design and simulate memory management layer
  RTL design and simulate processing layer

## Slide 43: Summary
Real world applications will require multiple artificial neural networks
  current solutions consume significant power and real-estate
Proposed a 3DIC solution that includes:
  Custom organized 3D-DRAM specification
  ANN specific data structures
  Purpose designed functions to accelerate a family of Artificial Neural Networks
  Architecture to take advantage of 3D technology
Overall performance and power improvement
  compared to GPU solutions and non-3D ASIC solutions
Notes: That concludes my presentation.
Thank you

## Slide 44: References

## Slide 45: Backup

## Slide 46: Deep Neural Network Backup

## Slide 47: Example DRAM Access Sequence

## Slide 48: Stack Bus
Downstrean and upstream buses
  OOB bus carries control
Buses carry control packets and data packets
  packets will be multiple clock cycles
Control packets used to configure PE
  special function and SIMD operations
  result information
Data Packets will carry arguments for special functions
  data to will be multiple cycles of two 32-bit words
Notes:   result information such as unicast or multicast, destination page
Return bus can be driven by all layers
  research will determine if bus is arbitrated or whether each layer buffers and forwards

## Slide 49: Example Image Recognition CNN
Example taken from Krizhevsky, Sutsever, Hinton 2012 [Kri12]
Seven layers but only first 3 layers shown
~60M parameters(~2Gb), ~2GFLOP

## Slide 50: Full ConvNet

## Slide 51: Cogent Confabulation Backup

## Slide 52: Summary
Cogent confabulation is used estimate the likelihood of an observation
The observation is a set of symbols with each symbol pulled from a Lexicon
  Lexicon can be unique to a symbol location or common to all observed symbols
Uses Knowledge bases which contain connections between lexicon symbols
  Each Connection known as a knowledge link and is analogous to a synapse
  Connection weight proportional to the coexistence likelihood
    Lexicon can be formed from any “feature(s)” but the literature refers to the observed symbols as “words”
  Can be used to estimate likelihood of observation or predict missing symbols based on observation

## Slide 53: Summary
Knowledge base connection weights are typically stored as log’s
  Likelihood calculation involves only additions
Can be quite memory intensive
  Knowledge base matrices are expected to be sparse so memory requirements reduced using compression
  Some recent work utilizing Cogent Confab on a simple robot navigation system showed compression of up to 1%

## Slide 54: Knowledge-base
Knowledge base matrix contains pairwise symbol likelihoods between Lexicon’s
  Matrix whose size is the lexicon-squared
  Entries are known as Knowledge Links
  Each entry is the likelihood of coexistence
  Each KB is sparse but can still be large
Knowledge (synapse) exists if non-zero entry in KB matrix
  Number of Knowledge Links is as important as likelihood value
Knowledge base constructed from counts of symbols and pairwise symbol coexistence
  Learning is simple (nothing like back-propagation)
  KL weights are relatively easy to calculate although log of weights is typically used to simplify likelihood calculations
  Potential for online learning if counts are maintained

## Slide 55: Likelihood
Each Knowledge Base contains likelihood of coexistence between symbols in the observation

## Slide 56: Design Backup

## Slide 57: TSV Power
from [Liu12]

## Slide 58: DiRAM4 Stack
from [Pat14]

## Slide 59: Detailed Block Diagram

## Slide 60: Scaling from [Sch14]

## Slide 61: Special Functions Backup

## Slide 62: Other Functions
The following special functions are provided to interoperate with the PE/SIMD
  Store to local registers/memory
  copy local registers/memory to DRAM

## Slide 63: Example Special Functions
The following special functions are required to accelerate our family of NN’s
  Fused MAC (FMA)
  ReLu
  Sigmoid
  Max
  Mean
  Odd-Even sort
  Merge Sort
  Sum
  ExpSum
    Softmax threshold
  Select n
    Find n likely candidates
  Count above threshold
    Find list of likely candidates
  A typical GPU solution used for CNNs will consume ~100-200W and with a GPU silicon area of ~550mm2 at 28nm
  As a benchmark we will target 28nm or 32nm depending on availability
Power
  we would like to improve GPU solution by >20x
  assuming 8 GPU’s means we will like to hit ~ 40W

## Slide 64: Operand Storage Backup

## Slide 65: Example Operands on the Stack Bus
If Stack bus width is 64 single precision words (2048b)
Words are arranged in pairs of operands (arg0/1)
  For example, arg0 will be the input ROI and arg1 will be the weights
PE function will be pre-configured prior to operand transmission
DRAM pages will be read and passed to stack bus either in parallel or serially
  neuron state page contains a set of neuron states and can be fanned out or directed to arg0
  weight page contains up to 32 weights and each word can fanned out or directed toward arg1

## Slide 66: Input/Weight Operand Storage

## Slide 67: Weight Operand Storage
We want to stream weights, inputs and pooling operands at line rate
Store pixel feature maps consecutively in a page
During activation calculation, words/features within a page are directed toward an EL
During pooling, words/features within a page are fanned out to all exec lanes
in DNNs, feature maps are typically multiples of 32 so both pooling and convolution can be performed relatively efficiently with our page size and memory arrangement

## Slide 68: Example Input Storage

## Slide 69: Example Kernel Storage

## Slide 70: Area and Power Backup

## Slide 71: Target Area and Power
Tezzaron DiRAM4 [Tez] Area and power is representative of a target DRAM
  ~12.5mm by 14mm provides approx 175mm2
  Assume 65% available before P/R leaves 113mm2

## Slide 72: Estimated DRAM Internal Power
Considering the DRAM Read path sequence shown previously (energy numbers from [Tez])
Internal DRAM Power
Our multi-CNN will likely use 54Tbps out of 131Tbps

## Slide 73: Stack Bus TSV Power
Assumptions:
  Assume Stack bus employs an invert bit to minimize transitions between cycles
  TSV energy based on [Liu12]

## Slide 74: DRAM Page Bus TSV Power
Assumptions:
  Assume bus employs an invert bit to minimize transitions between cycles
  Single TSV energy based on [Liu12]

## Slide 75: FMA Power/Area Estimate
Consider an FMA running at the Stack bus speed of ~1GHz, from [GH11] table 1

## Slide 76: FMA Power/Area Estimate
From [GH11] figure 10 scaling from 45nm to 32nm whilst maintaining the mm2/Gflop suggests a scaling factor of 0.53

## Slide 77: TSV Area
Power Delivery
  ~2000TSV’s ~0.1mm2
Stack Bus
  2737 signals
  Assume 2:1 for GND/VCC ~ 5500 TSV’s
  5um pitch ~ 0.14mm2/PE
  8.8mm2 for 64 PE’s
DRAM Bus
  4255 signals ~ 8500 TSV’s
  13.6mm2 for 64 Ports

## Slide 78: PE Area Estimates
For “other” PE control logic we used some estimates from a design used for the DARPA Cortical project
  example designs synthesized only at 65nm
  area estimates based on combinations of scaling numbers taken from [Sch14]
  assume FMA numbers are accurate
  SRAM 32 banks of 512x32 (could be much lower)
  Silicon area based on DiRAM4
  Target area includes adjustments for P/R and TSV’s
Scaling Estimates |  |  |  |  | 
 | Worst | Average Worst 2 | Average | Average Best 2 | Best
 | 32nm | 32nm | 32nm | 32nm | 32nm
SIMD | 1012658 | 435101 | 332716 | 232000 | 200000
DMA | 207519 | 155820 | 131872 | 106720 | 92000
stOp Control | 270677 | 203243 | 172008 | 139200 | 120000
MC | 165789 | 124486 | 105355 | 85260 | 73500
Cntl | 311278 | 233730 | 197809 | 160080 | 138000
SRAM | 417349 | 313375 | 265213 | 214628 | 185025
FMA | 304080 | 285835 | 258130 | 235155 | 202720
Chart: 
| Worst | Average Worst 2 | Average | Average Best 2 | Best
Estimated Area | 258.8247 | 168.5741 | 140.8099 | 112.8944 | 97.3228
Target Area | 175 | 175 | 175 | 175 | 175

## Slide 79: Power Summary
Power estimates based on experience and the following:
  Low activity in management layer as much of the time logic is passing data from DRAM to Stack bus
  TSV interconnect estimates include DRAM interface and stack bus
  PE estimate includes SIMD and SRAM estimates from DARPA project
  DRAM internal power based on anticipated activity and energy per operation from DiRAM4 spec
  FMA power based on [GH11]
The approximately 40W estimate is within performance and power management targets
Function | Power | Comment
Management Layer | 16 | Assumes logic is mainly passing data from DRAM to Stack bus
PE | 1.6 | Does not include FMA
FMA | 4.66 | from [GH11]
DRAM | 3.32 | from [Tez] and activity estimates
TSV Interconnects | 13.12 | based on [Liu12]
Total/PE | ~40W | 

## Slide 80: GPU Backup

## Slide 81: GPU Performance Backup
from [Far11]

## Slide 82: Spiking Backup

## Slide 83: Artificial Neural Networks Spiking
Information stored in connection delays and weights
Output of network a spike sequence
Output of neuron are spikes

## Slide 84: Artificial Neural Networks Spiking example

## Slide 85: DRAM Backup

## Slide 86: Custom Organized DRAM
DRAM’s have uncooperative rules
  Page open to page read command latency
  Page open to page close
  Page data read latency
Page open to page open times are long ~20nS
  Need to absorb PO-PO latency
  Multiple banks required to maximize bandwidth
  Need a lot of banks to arrange input arrays to avoid bank conflicts when reading ROI
Maintain bandwidth by interleaving banks
  We need to ensure data and kernels/weights are arranged appropriately
Buffer open pages prior to transmission on stack bus
Require operation size >> Data latency
  e.g. kernels typically > 192
  DiRAM4 Latency ~ 8 cycles
Notes: DRAM’s have uncooperative rules
  Page open to page read command latency
  Page open to page close
  Page data read latency
Page open to page open times are long ~20nS
  Need to absorb PO-PO latency
  Multiple banks required to maximize bandwidth
  Need a lot of banks to arrange input arrays to avoid bank conflicts when reading ROI
Maintain bandwidth by interleaving banks
  We need to ensure data and kernels/weights are arranged appropriately
Buffer open pages prior to transmission on stack bus
Require operation size >> Data latency
  e.g. kernels typically > 192
  DiRAM4 Latency ~ 8 cycles

## Slide 87: Mission Statement

## Slide 88
Current demonstrations of DNNs have set a benchmark for the size of neural networks to achieve useful, real-world tasks
The complexity of these neural networks is in some part driven by the available resources and there will be a need to provide power and area efficient solutions that allow the complexity of the neural networks to extend beyond the current levels.
Solutions to complex problems where artificial neural networks will be employed will involve multiple sensors each feeding neural networks.
A system of these artificial neural networks will be used as input to a larger system.
Power and space will be issues when these complex neural network systems are employed in most applications