## Slide 1: A 3DIC system to aid in the acceleration of systems that employ multiple instances of artificial neural networks
Final exam : Lee B. Baker
Advisor: Paul Franzon
Notes: I suspect most of us have seen reports on self-driving cars.
But how can a car determine whats in its surroundings?
One piece of technology that is and will be used is Artificial neural networks
These artificial neural networks allow the vehicle to recognize street signs, other vehicles, pedestrians, edges of the road, all the things you might need to safely navigate a 2-ton car.
The ability for artificial neural networks to perform that function in a timely fashion within reasonable power and space constraints is what I am going to talk about today.

## Slide 2: Introduction
Recently Artificial Neural networks (NN) have demonstrated superior performance in classification and function approximation
  Deep Neural Networks (DNN) have been very successful in image processing applications [Kri12]
  it is anticipated that DNNs will be employed more and more in self-driving cars
  Reinforcement learning is gaining popularity
  alphaGo employed reinforcement learning with deep neural networks [Mad14]
http://www.hackerboards.com
http://www.BGR.com
http://www.engadget.com
Notes: Now I mentioned self driving cars,
but recently ANN’s have also demonstrated efficacy when employed as a part of face recognition, text recognition and game playing systems
These ANN’s have demonstrated significant improvements over current state of the art.
Some example uses of ANN’s are the google car and you may also have recently seen the Go game system AlphaGo, which recently “beat” a Go master.
So ANN’s are being deployed as we speak and we should therefore consider them to be in the ascent phase of the technology life cycle.

## Slide 3: Introduction
Many applications will and do require multiple NN engines running at or near real-time
  drone scanning in many directions during navigation
    looking down different than looking forward??
  aircraft performing system diagnostics during flight
    observing thermal profiles
    observing vibrations
  cloud server processing multiple images when searching
  aircraft performing system diagnostics during flight
  text recognition system processing multiple pages of text
Notes: Many applications require information to be provided at or near real time or simply have large volumes of data to process.
This means these systems will require multiple ANN’s to be running concurrently
A vehicle will need real time feedback on its surroundings.
A cloud server performing text or image searches must provide feedback in seconds.
Text recognition may not have a real-time requirement but just the volume of work requires we process in parallel
to complete the work in a reasonable time

## Slide 4: Problem
Most useful ANNs are big
  100’s of thousands of artificial neurons
  real-time processing requires lots of memory bandwidth
Notes: Many applications require information to be provided at or near real time or simply have large volumes of data to process.
This means these systems will require multiple ANN’s to be running concurrently
A vehicle will need real time feedback on its surroundings.
A cloud server performing text or image searches must provide feedback in seconds.
Text recognition may not have a real-time requirement but just the volume of work requires we process in parallel
to complete the work in a reasonable time

## Slide 5: Problem
Most research focused on CNNs
  easier to implement
  can take advantage of SRAM
A lot of focus on server applications
  perhaps lots of research $$ available??
  server applications can take advantage of SRAM
Many DNNs are fully-connected [XX]
  limited SRAM benefit unless used in server applications (batch processing)
Notes: The problem is having a system implement multiple of these ANN’s in real time.
Effective ANN’s are big, they contains lots of neurons.
Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements when supporting useful NN’s (GPU ~100W)
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 6: Problem
Many embedded applications will/do have power, space and weight limitations
  to achieve near or at real-time processing, current solutions require high power and high real-estate
    GPU solutions have large real-estate and power requirements (~100-200W)
    ASIC’s target smaller network sizes and/or specific NN’s
    Both have memory bandwidth limitations
  multiple disparate ANNs means SRAM is of limited use
Notes: The problem is having a system implement multiple of these ANN’s in real time.
Effective ANN’s are big, they contains lots of neurons.
Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements when supporting useful NN’s (GPU ~100W)
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 7: Solution
3DIC Architecture
  reduces energy and area
  increase connectivity and bandwidth
3D-DRAM
  provide high bandwidth and large storage
Data Structures
  data structures to ensure neural network data can be accessed efficiency
Specialized processing layers
  provide special functions to aid in acceleration of target neural networks
Notes: This work proposes taking advantage of 3D IC technology.
This 3D architecture will include a custom organized 3D DRAM to store the neural network and Data structures designed to access that DRAM effectively.
The proposal also includes custom processing layers to perform the NN computations.
Using DRAM addresses the large network size requirement
and the 3D architecture ensures we can address bandwidth, space and power issues.
The custom processing layers will be targeted toward a family of ANN’s

## Slide 8: Solution
Can a 3D-DRAM be used effectively?
Can a useful system fit within the 3D stack?
How can we control such a system?
Notes: The primary contributions of this work is
- a custom organized 3DIC DRAM allowing us to provide the necessary memory bandwidth to process multiple ANN’s in real time
- data structures for storing parameters and neuron activation values
- a 3D architecture which will ensure the bandwidth provided by the custom memory can be processed at line rate by a processing layer customized to the functions required to process the target ANN’s
Combining these contributions will allow us to demonstrate a significant performance improvement overcurrent solutions

## Slide 9: Contribution
An extensible architecture that can simultaneously process multiple disparate real-time DNNs
  with low power and real estate demands
Proposed a custom 3D-DRAM providing a 64X bandwidth benefit compared to standard 3D-DRAM
  the 3D-DRAM could be employed in other applications
A DNN system solution that employs pure 3DIC technology
  providing power and performance benefits of remaining within a 3DIC stack
Custom instructions and data structures that facilitate operating directly out of 3D-DRAM
  provide the required processing bandwidth by ensuring effective use of the 3D-DRAM
  instruction format allow system functions to operate concurrently

## Slide 10: Outline
What are artificial Neural networks
Target Neural networks
State-of-the-art
System Architecture
  Problem
  Solution
System details
  3DIC DRAM and data structures
  3D Bus
  Manager
  Processing engine
Results
Summary

## Slide 11: Artificial Neural Networks
a network of processing elements inspired by the connectivity and processing observed in the brain
the processing elements or neurons are connected together to form a network
Notes: Neural networks are a mathematical model, but they are advertised as being inspired by neurons in the brain.
Mention this is the basic neuron model used is almost all ANN’s
Mention it has been well understood that when organized like this a network of ANN’s can be used to solve complex functions and classifiers
The terminology used is the neuron being considered is the post synaptic neuron when they are linear function approximators

## Slide 12: Artificial Neural Networks
the processing elements fall into two categories
  rate based neurons which try to capture the neuron behavior in the form of a number
    relatively simple to model
    information stored in the form of strength of connections
    easier to train and have shown high levels of efficacy in many applications
  spiking neurons which more closely emulate actual brain behavior
    model neural activity in the form of differential equations
    require numerical methods to solve although there have been attempts to employ analog circuits
    information stored in the form of strength and delay of connections
    complex and hard to train
In this work we are focusing on rate based ANNs
Notes: Keep this concise
Real neurons generate spikes
Believed that information is carried in spike rates
Rate coding is a simplification
    Rate-based neural network used when we see demonstrations from google etc.
Spiking considered more powerful

## Slide 13: Artificial Neural Networks Rate-based
Information stored in connection weights
Output of network is class probability or a value
Output of neuron is fixed value
Multiple layers of neurons
Outputs of each layer feeds next layer
Notes: Keep concise
Mention ReLu function

## Slide 14: Target ANN Type’s
This work has focused on the DNNs :
  Classifiers
  function approximators
Notes: DNN classifiers because of their performance in image recognition
ANN in reinforcement learning because of their use as value function approximator
and finally Cogent Confabulation and BsB because of their joint efficacy in a text recognition system

## Slide 15: Deep Neural Network Classifiers
Currently the most popular ANN
  trained offline
Used in image recognition
  Convolutional NN’s have been very successful in classification
  locally-connected NN’s also used in face recognition
  fully-connected popular (MLP and LSTM)
This work will focus on inference
Notes: Trained offline
Used for inference
Deep Neural Networks (DNNs) are feed-forward multi-layered neural networks
Each layer identifies features in the previous layer
  Features are identified by convolving a filter (kernel) over a Region of Interest (ROI) in the input
  CNNs are a class of DNNs that use the same feature kernel across the entire input layer(s)
Layers separated using a non-linearity (tanh, sigmoid, ReLu)
  ReLu is becoming a popular choice
Final layers are typically fully connected classifiers
  in classifiers outputs are one-hot softmax probability
    each output represents a class such as Tank, cannon, house, pickup truck, dog, hoagie
  in function approximator each output represents a value
    in reinforcement learning, the value represents an action reward

## Slide 16: Deep Neural Networks
Current implementations either use GPU’s or low capacity ASIC implementations
GPU’s are typically general purpose devices and consume high power
  GPU’s do lend themselves to convolution
  typically one GPU required per ANN
ASIC implementations target larger networks by using multiple devices
  usually assume local SRAM which limits network size
  some implementations target specific NN’s, usually CNNs
System includes special functions used in the neuron activation process
  multiply/accumulates and ReLu
  softmax function

## Slide 17: Outline

## Slide 18: State of the Art
ASICs
  Most employ arrays of processors
  Some target specific ANNs
  Most cannot support useful sized NNs
  Many process data from local SRAM memory which often consumes >60% of silicon area

## Slide 19: State of the Art ASIC’s
ASIC’s
Eyeriss[Che16]
NeuroCube[Kim16]

## Slide 20: State of the Art ASIC’s
Those that utilize DRAM to implement useful sized NN’s
  NeuroCube1 uses HMC 3D-DRAM and an NoC to distribute data to the processing array thus limiting bandwidth
  Eyeriss2 discusses DRAM accesses but their focus is on the convolution operation and they do not address “other” NN’s
  NnSP3 uses cache between DRAM and SRAM and is limited by DRAM bandwidth
Eyeriss and Neuflow4 limit their support to CNNs and in the case of Eyeriss only supports the convolution
  will not support locally-connected ANNs
More recent designs such as NeuroCube are approaching a performance of ~<40GOPS/W
  more interesting number as it implements a meaningful NN
Neuflow approaches a performance of ~200GOPS/W
  not meaningful as it cannot support useful size NN’s
Notes: What measure would you use?

## Slide 21: State of the Art
GPU’s
  NVidia seems to be putting some focus on CNNs especially in image processing
  Will still be limited by memory bandwidth although they are starting to utilize 3D-DRAM
    2.5D solution using HBM memory
    will be restricted by bandwidth of HBM (~2Tbps) and interposer
    actual uses have demonstrated you cannot utilize the full processing capability of a GPU
  Power of GPU solution ~100-200W
Notes: Titan GPU designed for 4Tbps

## Slide 22: State of the Art GPU’s
GPU’s target the general market and employ infrastructures not necessary for NN implementation
  we associate power of GPU solution ~100-200W
  general purpose architecture makes it hard/impossible to make full use of theoretical performance
[Far11]

## Slide 23: State of the Art
Current state-of-the art ASIC’s and GPU’s do not provide the capacity and efficiency to provide a solution requiring multiple useful NN’s to be computed in real-time

## Slide 24: Outline

## Slide 25: Problem
System solution requiring multiple NN’s
  Consider a system that requires ~8 DNNs[Boj16]
  ~16Gb of memory
  ~100W per GPU suggests >800W total power
Real-Time
  Image needs to be processed ~16mS (60 frames/sec)
  Allowing ~10mS for classification requires ~1700GFLOPS1
  Required Memory bandwidth ~54Tbps
Current 3D-DRAM memory technology bandwidth
  HMC – SERDES~2Tbps
  HBM – wide DDR ~2Tbps
  Tezzaron DiRAM4 – wide DDR – 4Tbps

## Slide 26: Solution
Utilize 3DIC technology
Architecture includes:
  Custom organized 3D-DRAM specification
  Data Structures specific to each ANN
  Management Layer for configuration and control
  Processing layer(s) targeted toward a family of ANNs
    array of processing engines (PE) with special streaming functions
    PE will include small CPU to process non hot-spot functions and provide some generality
http://www.electroiq.com/
Notes:     Mention multiported
    Memory layers, control layer and processing layer could use different technology
    SSF’s will operate directly on data read from stack bus
    To increase bus widths, increase bandwidth while minimizing interface power
provide access to entire page rather than cache-line
there will be power considerations by not taking advantage of some reuse of data in local memory but I believe the performance benefits will outweigh the disadvantages
    Special streaming functions will also have the ability to operate on data in processing layers expected small amount of local memory
    avoid DRAM page open latency by using a highly banked DRAM and arranging data in memory to allow back-to-back page opens
    Careful consideration of layer state and kernel parameters required to maximize DRAM bandwidth

## Slide 27: Outline

## Slide 28: DRAM Ports, Bus Widths and PE Array Size
Determined how many PE’s required to support bandwidth needs
  based on available GOPS, current DRAM technology and reasonable operating frequency
Size data width to provide enough operands to each execution lanes (EL)
Estimated 64-port memory each supporting a processing engine with 32 execution lanes
Review DRAM operations to stream data for power dissipation
Notes:     1.7 102 OPS
    assume 1GHz
    1700 OP/cycle => 2048 execution units
    each of the 64 ports needs to support 32 execution lanes
Note:
Initial discussion with 3D-DRAM supplier suggests idea is achievable

## Slide 29: Solution Block Diagram
Total downstream B/W
131Tbps
Array of processing engines
(PE)
Custom organized DRAM
Management Layer

## Slide 30: 3D Configuration
Array of processing engines
(PE)
Custom organized DRAM
Management
Layer

## Slide 31: Example DRAM Access Sequence

## Slide 32: 3D Stack Bus

## Slide 33: Stack Bus
Each processing column has a downstream and upstream stack bus
  Downstream 20481 bit running at 1GHz providing131Tbps raw system bandwidth
  Upstream bus 5122 bits running at 1GHz
    result bandwidth ~1/100th of operand bandwidth

## Slide 34: Stack Bus
Downstrean and upstream buses
Buses carry control packets and data packets
  packets will be multiple clock cycles
Control packets used to configure PE
  special function and SIMD operations
  result information
Data Packets will carry arguments for special functions
  data to will be multiple cycles of two 32-bit words
Notes:   result information such as unicast or multicast, destination page
Return bus can be driven by all layers
  research will determine if bus is arbitrated or whether each layer buffers and forwards

## Slide 35: Processing Layer

## Slide 36: Special Functions in PE
Special Functions are designed to operate on data from the Stack bus
  operate at line rate from downstream bus
  perform computations directly as data is read from memory
  avoid need for large local SRAM in PE
  result is passed to “small” local memory or registers for later processing by SIMD
  result sent to upstream bus
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 37: FEASIBILITY : POWER AND AREA ESTIMATES

## Slide 38: Power Summary
Function | Power | Comment
Management Layer | 16 | Assumes logic is mainly passing data from DRAM to Stack bus
PE | 1.6 | Does not include FMA
FMA | 4.66 | from [GH11]
DRAM | 3.32 | from [Tez] and activity estimates
TSV Interconnects | 13.12 | based on [Liu12]
Total/PE | ~40W | 
Power estimates based on experience and the following:
  Low activity in management layer as much of the time logic is passing data from DRAM to Stack bus
  TSV interconnect estimates include DRAM interface and stack bus
  PE estimate includes SIMD and SRAM estimates from DARPA project
  DRAM internal power based on anticipated activity and energy per operation from DiRAM4 spec
  FMA power based on [GH11]

## Slide 39: Area
Anticipate the processing layer to be primary concern
  Total area of processor layer based on DiRAM4
  Tezzaron DiRAM4 [Tez] Area and power is representative of a target DRAM
  ~12.5mm by 14mm provides approx 175mm2
For “other” PE control logic we used some estimates from a design used for the DARPA Cortical project
  example designs synthesized only at 65nm and area estimates based on combinations of various scaling number estimates taken from [Sch14]
  assume FMA numbers are accurate
  SRAM 32 banks of 512x32 (could be much lower)
  Target area includes adjustments for P/R and TSV’s
Processing Layer area estimate exceeds available only under worst case scaling
  low risk??
Chart: 
| Worst | Average Worst 2 | Average | Average Best 2 | Best
Estimated Area | 258.8247 | 168.5741 | 140.8099 | 112.8944 | 97.3228
Target Area | 175 | 175 | 175 | 175 | 175

## Slide 40: Outline
What are artificial Neural networks
Target Neural networks
State-of-the-art
Proposed Architecture
  Problem
  Solution
Preliminary Work
  3DIC DRAM and data structures
  3D Stack Bus
  Processing Layer
Research Plan
Summary

## Slide 41: Research
Specify a custom organization of a 3DIC DRAM
  provide a specification showing memory organization, bus widths
Research and propose Data Structures to exploit DRAM capacity
  provide data structure descriptions for each of the targeted ANNs
Propose 3D architecture to take advantage of DRAM capacity and bandwidth
  RTL design and simulate memory management layer
  RTL design and simulate processing layer

## Slide 42: Outline
What are artificial Neural networks
Target Neural networks
State-of-the-art
Proposed Architecture
  Problem
  Solution
Preliminary Work
  3DIC DRAM and data structures
  3D Stack Bus
  Processing Layer
Research Plan
Summary

## Slide 43: Summary
Real world applications will require multiple artificial neural networks
  current solutions consume significant power and real-estate
Proposed a 3DIC solution that includes:
  Custom organized 3D-DRAM specification
  ANN specific data structures
  Purpose designed functions to accelerate a family of Artificial Neural Networks
  Architecture to take advantage of 3D technology
Overall performance and power improvement
  compared to GPU solutions and non-3D ASIC solutions
Notes: That concludes my presentation.
Thank you

## Slide 44: References

## Slide 45: Backup

## Slide 46: Deep Neural Network Backup

## Slide 47: Example Image Recognition CNN
Example taken from Krizhevsky, Sutsever, Hinton 2012 [Kri12]
Seven layers but only first 3 layers shown
~60M parameters(~2Gb), ~2GFLOP

## Slide 48: Full ConvNet

## Slide 49: Cogent Confabulation Backup

## Slide 50: Summary
Cogent confabulation is used estimate the likelihood of an observation
The observation is a set of symbols with each symbol pulled from a Lexicon
  Lexicon can be unique to a symbol location or common to all observed symbols
Uses Knowledge bases which contain connections between lexicon symbols
  Each Connection known as a knowledge link and is analogous to a synapse
  Connection weight proportional to the coexistence likelihood
    Lexicon can be formed from any “feature(s)” but the literature refers to the observed symbols as “words”
  Can be used to estimate likelihood of observation or predict missing symbols based on observation

## Slide 51: Summary
Knowledge base connection weights are typically stored as log’s
  Likelihood calculation involves only additions
Can be quite memory intensive
  Knowledge base matrices are expected to be sparse so memory requirements reduced using compression
  Some recent work utilizing Cogent Confab on a simple robot navigation system showed compression of up to 1%

## Slide 52: Knowledge-base
Knowledge base matrix contains pairwise symbol likelihoods between Lexicon’s
  Matrix whose size is the lexicon-squared
  Entries are known as Knowledge Links
  Each entry is the likelihood of coexistence
  Each KB is sparse but can still be large
Knowledge (synapse) exists if non-zero entry in KB matrix
  Number of Knowledge Links is as important as likelihood value
Knowledge base constructed from counts of symbols and pairwise symbol coexistence
  Learning is simple (nothing like back-propagation)
  KL weights are relatively easy to calculate although log of weights is typically used to simplify likelihood calculations
  Potential for online learning if counts are maintained

## Slide 53: Likelihood
Each Knowledge Base contains likelihood of coexistence between symbols in the observation

## Slide 54: Design Backup

## Slide 55: TSV Power
from [Liu12]

## Slide 56: DiRAM4 Stack
from [Pat14]

## Slide 57: Detailed Block Diagram

## Slide 58: Scaling from [Sch14]

## Slide 59: Special Functions Backup

## Slide 60: Other Functions
The following special functions are provided to interoperate with the PE/SIMD
  Store to local registers/memory
  copy local registers/memory to DRAM

## Slide 61: Example Special Functions
The following special functions are required to accelerate our family of NN’s
  Fused MAC (FMA)
  ReLu
  Sigmoid
  Max
  Mean
  Odd-Even sort
  Merge Sort
  Sum
  ExpSum
    Softmax threshold
  Select n
    Find n likely candidates
  Count above threshold
    Find list of likely candidates
  A typical GPU solution used for CNNs will consume ~100-200W and with a GPU silicon area of ~550mm2 at 28nm
  As a benchmark we will target 28nm or 32nm depending on availability
Power
  we would like to improve GPU solution by >20x
  assuming 8 GPU’s means we will like to hit ~ 40W

## Slide 62: Operand Storage Backup

## Slide 63: Example Operands on the Stack Bus
If Stack bus width is 64 single precision words (2048b)
Words are arranged in pairs of operands (arg0/1)
  For example, arg0 will be the input ROI and arg1 will be the weights
PE function will be pre-configured prior to operand transmission
DRAM pages will be read and passed to stack bus either in parallel or serially
  neuron state page contains a set of neuron states and can be fanned out or directed to arg0
  weight page contains up to 32 weights and each word can fanned out or directed toward arg1

## Slide 64: Input/Weight Operand Storage

## Slide 65: Weight Operand Storage
We want to stream weights, inputs and pooling operands at line rate
Store pixel feature maps consecutively in a page
During activation calculation, words/features within a page are directed toward an EL
During pooling, words/features within a page are fanned out to all exec lanes
in DNNs, feature maps are typically multiples of 32 so both pooling and convolution can be performed relatively efficiently with our page size and memory arrangement

## Slide 66: Example Input Storage

## Slide 67: Example Kernel Storage

## Slide 68: Area and Power Backup

## Slide 69: Target Area and Power
Tezzaron DiRAM4 [Tez] Area and power is representative of a target DRAM
  ~12.5mm by 14mm provides approx 175mm2
  Assume 65% available before P/R leaves 113mm2

## Slide 70: Estimated DRAM Internal Power
Considering the DRAM Read path sequence shown previously (energy numbers from [Tez])
Internal DRAM Power
Our multi-CNN will likely use 54Tbps out of 131Tbps

## Slide 71: Stack Bus TSV Power
Assumptions:
  Assume Stack bus employs an invert bit to minimize transitions between cycles
  TSV energy based on [Liu12]

## Slide 72: DRAM Page Bus TSV Power
Assumptions:
  Assume bus employs an invert bit to minimize transitions between cycles
  Single TSV energy based on [Liu12]

## Slide 73: FMA Power/Area Estimate
Consider an FMA running at the Stack bus speed of ~1GHz, from [GH11] table 1

## Slide 74: FMA Power/Area Estimate
From [GH11] figure 10 scaling from 45nm to 32nm whilst maintaining the mm2/Gflop suggests a scaling factor of 0.53

## Slide 75: TSV Area
Power Delivery
  ~2000TSV’s ~0.1mm2
Stack Bus
  2737 signals
  Assume 2:1 for GND/VCC ~ 5500 TSV’s
  5um pitch ~ 0.14mm2/PE
  8.8mm2 for 64 PE’s
DRAM Bus
  4255 signals ~ 8500 TSV’s
  13.6mm2 for 64 Ports

## Slide 76: PE Area Estimates
For “other” PE control logic we used some estimates from a design used for the DARPA Cortical project
  example designs synthesized only at 65nm
  area estimates based on combinations of scaling numbers taken from [Sch14]
  assume FMA numbers are accurate
  SRAM 32 banks of 512x32 (could be much lower)
  Silicon area based on DiRAM4
  Target area includes adjustments for P/R and TSV’s
Scaling Estimates |  |  |  |  | 
 | Worst | Average Worst 2 | Average | Average Best 2 | Best
 | 32nm | 32nm | 32nm | 32nm | 32nm
SIMD | 1012658 | 435101 | 332716 | 232000 | 200000
DMA | 207519 | 155820 | 131872 | 106720 | 92000
stOp Control | 270677 | 203243 | 172008 | 139200 | 120000
MC | 165789 | 124486 | 105355 | 85260 | 73500
Cntl | 311278 | 233730 | 197809 | 160080 | 138000
SRAM | 417349 | 313375 | 265213 | 214628 | 185025
FMA | 304080 | 285835 | 258130 | 235155 | 202720
Chart: 
| Worst | Average Worst 2 | Average | Average Best 2 | Best
Estimated Area | 258.8247 | 168.5741 | 140.8099 | 112.8944 | 97.3228
Target Area | 175 | 175 | 175 | 175 | 175

## Slide 77: Power Summary
Power estimates based on experience and the following:
  Low activity in management layer as much of the time logic is passing data from DRAM to Stack bus
  TSV interconnect estimates include DRAM interface and stack bus
  PE estimate includes SIMD and SRAM estimates from DARPA project
  DRAM internal power based on anticipated activity and energy per operation from DiRAM4 spec
  FMA power based on [GH11]
The approximately 40W estimate is within performance and power management targets
Function | Power | Comment
Management Layer | 16 | Assumes logic is mainly passing data from DRAM to Stack bus
PE | 1.6 | Does not include FMA
FMA | 4.66 | from [GH11]
DRAM | 3.32 | from [Tez] and activity estimates
TSV Interconnects | 13.12 | based on [Liu12]
Total/PE | ~40W | 

## Slide 78: GPU Backup

## Slide 79: GPU Performance Backup
from [Far11]

## Slide 80: Spiking Backup

## Slide 81: Artificial Neural Networks Spiking
Information stored in connection delays and weights
Output of network a spike sequence
Output of neuron are spikes

## Slide 82: Artificial Neural Networks Spiking example

## Slide 83: DRAM Backup

## Slide 84: Custom Organized DRAM
DRAM’s have uncooperative rules
  Page open to page read command latency
  Page open to page close
  Page data read latency
Page open to page open times are long ~20nS
  Need to absorb PO-PO latency
  Multiple banks required to maximize bandwidth
  Need a lot of banks to arrange input arrays to avoid bank conflicts when reading ROI
Maintain bandwidth by interleaving banks
  We need to ensure data and kernels/weights are arranged appropriately
Buffer open pages prior to transmission on stack bus
Require operation size >> Data latency
  e.g. kernels typically > 192
  DiRAM4 Latency ~ 8 cycles
Notes: DRAM’s have uncooperative rules
  Page open to page read command latency
  Page open to page close
  Page data read latency
Page open to page open times are long ~20nS
  Need to absorb PO-PO latency
  Multiple banks required to maximize bandwidth
  Need a lot of banks to arrange input arrays to avoid bank conflicts when reading ROI
Maintain bandwidth by interleaving banks
  We need to ensure data and kernels/weights are arranged appropriately
Buffer open pages prior to transmission on stack bus
Require operation size >> Data latency
  e.g. kernels typically > 192
  DiRAM4 Latency ~ 8 cycles

## Slide 85: Mission Statement

## Slide 86
Current demonstrations of DNNs have set a benchmark for the size of neural networks to achieve useful, real-world tasks
The complexity of these neural networks is in some part driven by the available resources and there will be a need to provide power and area efficient solutions that allow the complexity of the neural networks to extend beyond the current levels.
Solutions to complex problems where artificial neural networks will be employed will involve multiple sensors each feeding neural networks.
A system of these artificial neural networks will be used as input to a larger system.
Power and space will be issues when these complex neural network systems are employed in most applications