## Slide 1: A 3DIC system to aid in the acceleration of systems that employ multiple instances of artificial neural networks
Final oral exam: Lee B. Baker
Date: 28th February 2018
PhD Committee:
Dr. W. Alexander, Dr. G. Byrd,
Dr. P. Franzon(Chair), Dr. R. Warr

## Slide 2: Introduction
Recently Artificial Neural networks (NN) have demonstrated superior performance in classification and function approximation
  Deep Neural Networks (DNN) have been very successful in image processing applications [Kri12]
  it is anticipated that DNNs will be employed more and more in self-driving cars
  Reinforcement learning is gaining popularity
  alphaGo employed reinforcement learning with deep neural networks [Mad14]
http://www.hackerboards.com
http://www.BGR.com
http://www.engadget.com
Notes: I suspect most of us have heard of ANNs and their use in applications such as self-driving cars.
The ability for artificial neural networks to perform in a timely fashion within reasonable power and space constraints is what I am going to talk about today.
I am going to present a system that is able to accelerate multiple instances of disparate useful sized artificial neural networks and provide power and/or area benefits over current state-of-the-art

## Slide 3: Introduction
What about applications that will and do require multiple NN processors running at or near real-time?
  drone scanning in many directions during navigation
    looking down different than looking forward??
  aircraft performing system diagnostics during flight
    observing thermal profiles
    observing vibrations
  airport security
    face recognition
    body thermal profiles
    motion
Notes: If ANNs fulfill their potential they will be employed in embedded applications performing various system tasks.
So these embedded systems will employ multiple disparate useful sized ANNs that need to be processed at or near real time.

## Slide 4: Introduction
Most useful ANNs are big
  100’s of thousands of artificial neurons
  real-time processing requires large amounts of memory bandwidth and storage
  DRAM is required
  Most implementations employ SRAM for local memory
from [27]
Notes: Most ANNs are big and the trend is that they are becoming larger and deeper
There is general acceptance that DRAM needs to be used to stored the ANN parameters
But many implementations have focused on using SRAM as an intermediate store to isolate the system from the slower DRAM.
Now this has proved to be very effective when there are reuse opportunities where the SRAM can be loaded from DRAM then accessed multiple times before having to go back to the slower DRAM.
The main reuse opportunities come in the form of shared parameters and batch processing.
Batch processing occurs when multiple requests are made to the same ANN, such as in cloud application.
Parameter reuse occurs when the same connection weights are used at different locations of the ANN

## Slide 5: ANN Types
Convolutional neural networks
  shared filter kernel allows reuse
  classifier stages are fully-connected – no reuse
  non-shared kernels – no reuse [42][27]
from [27]
Notes: First, we are considering embedded systems that will not have batch processing opportunities
We will have reuse in the form of shared parameters in Convolutional NNs where the same feature kernels are applied across the input.
But reuse isn’t available when we have CNNs with non-shared kernels

## Slide 6: ANN Types
DNNs and LSTM
  fully-connected - no reuse
  classifier stage in CNNs
from [27]
Notes: There are other types of ANNs that do not provide reuse opportunities such as and fully-connected DNNs such as LSTM.
Our mission is to be able to support all types of ANNs
So the embedded application's we are targeting have the potential to expose the limitations of these SRAM-based implementations

## Slide 7: Research
Most research focused on CNNs
  can take advantage of SRAM using parameter reuse
A lot of focus on server applications
  perhaps lots of research $$ available??
  server applications can take advantage of SRAM for batch processing
But many DNNs are fully-connected [1]
  LSTM and MLPs
  classifier stage of all ANNs including CNN
  CNNs represented only 5% of cloud workload [1]

## Slide 8: Mission Statement
Real world embedded applications will require multiple disparate NNs to be solved simultaneously
  If ANNs fulfill their potential, they will be used for various system functions
Need the capacity provided by DRAM
  Avoid dependency on SRAM
  SRAM is easy to use, but capacity limitations impose ANN size restrictions.
Need to consider the system impact
  Research often focuses on point problems. Need to consider interaction between blocks.
Notes: During the creation of this works system, when I had the urge to add SRAM because it made things easier, I forced myself to think how I could solve it with just the DRAM
This work is proposing using 3DIC technology, and in this case I felt it was important to also get a very good feel for the area associated with such a system

## Slide 9: Problem
Many embedded applications will/do have power, space and weight limitations
  to achieve near or at real-time processing, current solutions require high power and high real-estate
    GPU solutions large and high power
    ASIC’s better than GPUs
  Both have memory bandwidth or capacity limitations when reuse opportunities do not exist
Notes: Current implementations typically employ graphics processors or application specific integrated circuits.
  GPU solutions have large real-estate and power requirements
ASIC’s on the other hand can be designed to efficiently perform the ANN processing but they typically target smaller network sizes and/or specific NN’s
So there isn't currently a solution out there that can support processing multiple ANN’s in real time within reasonable power and size constraints.

## Slide 10: Solution
3DIC Architecture
  reduces energy and area
  increase connectivity and bandwidth
3D-DRAM
  provide high bandwidth and large storage
  operate directly out of DRAM
Data Structures
  data structures to ensure neural network data can be accessed efficiency
Specialized processing layers
  provide special functions to aid in acceleration of target neural networks
Notes: This work proposes taking advantage of 3D IC technology.
This 3D architecture will include a custom organized 3D DRAM to store the neural network and Data structures designed to access that DRAM effectively.
The proposal also includes custom processing layers to perform the NN computations.
Using DRAM addresses the large network size requirement
and the 3D architecture ensures we can address bandwidth, space and power issues.
The custom processing layers will be targeted toward a family of ANN’s

## Slide 11: Feasibility
Can a 3D-DRAM be used effectively?
Can a useful system fit within the 3D stack footprint?
How can we control such a system?
Notes: The primary contributions of this work is
- a custom organized 3DIC DRAM allowing us to provide the necessary memory bandwidth to process multiple ANN’s in real time
- data structures for storing parameters and neuron activation values
- a 3D architecture which will ensure the bandwidth provided by the custom memory can be processed at line rate by a processing layer customized to the functions required to process the target ANN’s
Combining these contributions will allow us to demonstrate a significant performance improvement overcurrent solutions

## Slide 12: Contribution
An extensible architecture that can simultaneously process multiple disparate real-time DNNs
Proposed a custom 3D-DRAM providing a ~32X bandwidth benefit compared to standard 3D-DRAM
A DNN system solution that employs pure 3DIC technology
Custom instructions and data structures that facilitate operating directly out of 3D-DRAM

## Slide 13: Outline
What are artificial Neural networks
Target application and ANN type’s
State-of-the-art
System Architecture
  Problem
  Solution
System details
  3DIC DRAM and data structures
  3D Bus
  Manager
  Processing engine
Results
Summary

## Slide 14: Artificial Neural Networks
a network of processing elements inspired by the connectivity and processing observed in the brain
the processing elements or neurons are connected together to form a network
[7][34]
[7][34]
[7][34]
Notes: Neural networks are a mathematical model, but they are advertised as being inspired by neurons in the brain.
Mention this is the basic neuron model used is almost all ANN’s
Mention it has been well understood that when organized like this a network of ANN’s can be used to solve complex functions and classifiers
The terminology used is the neuron being considered is the post synaptic neuron when they are linear function approximators

## Slide 15: Artificial Neural Networks
the processing elements fall into two categories
  rate based[7][34] neurons which try to capture the neuron behavior in the form of a number
    relatively simple to model
    easier to train and have shown high levels of efficacy in many applications
  spiking neurons[7][34] which more closely emulate actual brain behavior
    model neural activity in the form of differential equations
    require numerical methods to solve although there have been attempts to employ analog circuits
In this work we are focusing on rate based ANNs
Notes: Keep this concise
Real neurons generate spikes
Believed that information is carried in spike rates
Rate coding is a simplification
    Rate-based neural network used when we see demonstrations from google etc.
Spiking considered more powerful

## Slide 16: Summary : Target application and ANN type’s
Embedded systems
  not cloud based
  assumes multiple tasks are being performed
  requires multiple disparate ANNs
  inference only
This work has focused on support for:
  fully- and locally-connected DNNs
  can be extended to support LSTMs
Notes: DNN classifiers because of their performance in image recognition
ANN in reinforcement learning because of their use as value function approximator
and finally Cogent Confabulation and BsB because of their joint efficacy in a text recognition system

## Slide 17: State-of-the-art
Current implementations either use GPU’s or low capacity ASIC implementations
GPU’s are typically general purpose devices and consume high power
  GPU’s do lend themselves to convolution when weights are shared
  Lemma: ASICs always perform better than GPUs
ASIC implementations target larger networks by using multiple devices
  usually local SRAM which limits network size
  some/most implementations target specific NN’s, usually CNNs

## Slide 18: State of the Art ASIC’s
ASIC’s
Eyeriss[11]
NeuroCube[24]

## Slide 19: State of the Art ASIC’s
NeuroStream[3]
  acknowledges DRAM is required for useful DNNs
  uses HBM 3D-DRAM along with local SRAM
  depends on SRAM for performance
Google TPU[1]
  assumes large levels of batch processing
  8-bit processing
  fully-connected NNs represent very high percentage
  acknowledges performance degradation using fully-connected
DaDiannao[10]
  uses embedded DRAM but still requires up to 64 for useful DNNs
  high internal bandwidth but dissipates high power when scaling to useful-sized ANNs
Notes: Mention focus on more recent devices

## Slide 20: State of the Art
Current state-of-the art ASIC’s and GPU’s do not provide the capacity and bandwidth to provide a solution requiring multiple useful disparate ANN’s to be computed in real-time
Goldilocks principle
  need balance of bandwidth and storage
  need to read all parameters in sample time for real-time processing
  Currently SOA bandwidth too low or too high

## Slide 21: System Requirements
System solution requiring multiple NN’s
  binary32 number format
  ~8GB of memory for baseline ANN
  real-time processing : ~16mS (60 frames/sec)
  ~26Tbps memory bandwidth for baseline ANN
Current 3D-DRAM memory technology bandwidth
  HMC – SERDES~2Tbps – too low
  HBM – wide DDR ~2Tbps – too low
  Tezzaron DiRAM4[14] – wide DDR – 4Tbps – too low
Propose Customized DiRAM4
  expose more of the page
  take advantage of high density TSVs

## Slide 22: Architecture Blocks
Proposed Customizations to standard DiRAM4 3D-DRAM
Data Structures and Instructions to support efficient use of DRAM
Management Layer for configuration and control
  DRAM controller
  Instruction decoder
Processing layer targeted toward DNNs
  streaming functions operate directly on data
    multiply/accumulates ANe activation
    multiply for softmax
  additional special functions in SIMD used in the neuron activation process
    ReLu for ANe activation
    add, divide and exponent for softmax function
    compare for pooling
Notes:     Mention multiported
    Memory layers, control layer and processing layer could use different technology
    SSF’s will operate directly on data read from stack bus
    To increase bus widths, increase bandwidth while minimizing interface power
provide access to entire page rather than cache-line
there will be power considerations by not taking advantage of some reuse of data in local memory but I believe the performance benefits will outweigh the disadvantages
    Special streaming functions will also have the ability to operate on data in processing layers expected small amount of local memory
    avoid DRAM page open latency by using a highly banked DRAM and arranging data in memory to allow back-to-back page opens
    Careful consideration of layer state and kernel parameters required to maximize DRAM bandwidth

## Slide 23: Main memory
The 3D-DRAM is the Tezzaron DiRAM4
  64 disjoint 1Gb memory ports
  System has 64 sub-systems each operating on one memory port
Suggested Customizations for a 3D-DRAM
  Standard DiRAM4 port is 32bits @ 1GHz
  We suggest widen to 2048 bits and use high-density TSVs
  Entire page in one access using burst-of-2
  Raw bandwidth ~2Tbps per port

## Slide 24: System Solution
System has 64 sub-systems (SSC) each operating on one memory port
  ANNs split over sub-systems
  SSCs communicate over local NoC in each Manager
Sub-system (SSC) has a Manager and PE
  Instruction Decode in Manager
    contains information on how to process a group of ANes
  Wide Data-path between DRAM, Manager and PE
    data for 32 execution lanes with two arguments per lane
  PE performs ANe state operations
    process a group of ANes
    able to perform a MAC operation between a weight and ANe state every cycle
Notes: able to process a group of 32 ANes each instruction
return data contains up to 32 words
where are weights, ANe states and result stored

## Slide 25: 3D Physical Configuration
Processing engine
(PE) layer
Customized
3D-DRAM
Management
layer

## Slide 26: Sub-System Column (SSC)
Consists of DRAM, manager and processing engine (PE)
logical
physical

## Slide 27: Solution Block Diagram
Total downstream B/W
64Tbps
Processing engine layer
(PE)
Customized DRAM
Management Layer

## Slide 28: System Connectivity
Processing engine layer
(PE)
Customized
DRAM
Management Layer

## Slide 29: Architecture Requirements
Need to absorb DRAM latency
  separate memory requests from read/write data
Instruction spawns multiple commands to dependent tasks
  concurrently pre-fetch data, prepare PE, prepare Return Data Processor
  all operations have an associated tag
Need to describe parameter and state storage
  assume input stored in row-major fashion
Network-on-Chip
  needed for ANe state replication to all dependent SSCs

## Slide 30: Instructions
Instructions consist of descriptors
Descriptors used to control modules which take part in the instruction
Descriptors contain tuples which contain the details

## Slide 31: Instruction Decode
Two types of instruction
  Configuration
  Compute
Manager sends descriptors to dependent block(s)
  may not parse descriptor if not relevant to manager
  manager knows descriptor dependencies and sends to modules participating in instruction
Configuration Instruction
  send descriptor to manager control block
  used for synchronization and data transfers
Compute Operation
  send descriptor(s) to blocks participating in ANe state computation
  OP
    send descriptor to PE
  Memory Read
    identify target execution lane and send descriptor to one of two memory read controller
  Memory Write
    send descriptor to return data processor

## Slide 32: Compute Instruction

## Slide 33: Configuration
Supports both synchronization and data transfer

## Slide 34: Data Storage and access
Inputs and ANe states stored in row-major
  two address increment mechanisms
Weights for a group of ANes are interleaved

## Slide 35: Storage descriptors
Used to describe how data is read/written
Used for both parameter and ANe state storage
  instruction contains pointer to storage descriptor
  each SSC has a set of storage descriptors
  instruction/NoC carry pointer, not address, length etc.

## Slide 36: NoC
Four ports
  connections to adjacent SSC
  fixed routing table
  can be reconfigured based on performance
  good area for additional research

## Slide 37: Manager Layer
Decodes instructions
  sub-descriptors are sent to dependent blocks
Reads and writes to main memory
Communicates to host and other SSCs
Decode
Memory read
Memory Write
Return Data
processor
Main
Controller
NoC
OOB
Data
To
PE
Data
from
PE
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 38: Manager Layer
Decodes instructions
  sub-descriptors are sent to dependent blocks
Reads and writes to main memory
Communicates to host and other SSCs
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 39: DRAM Customizations
Expose more of the page
  Each burst-of-2 read transfers entire page
  Need to accommodate idle time during Page Close
  Employ TSVs for wide bus
Provide write masks
  To avoid Read-Modify-Write
[13]
[13]
Customize
Access
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 40: DRAM Customizations
Expose more of the page
  Each burst-of-2 read transfers entire page
  Need to accommodate idle time during Page Close
  Employ TSVs for wide bus
Provide write masks
  To avoid Read-Modify-Write
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 41: Processing (PE) Layer
Streaming operations operate directly on data
SIMD Wrapper performs post stOp tasks
Streaming
Operations
SIMD
Special
Functions
PE
Controller
SIMD
Return
Data
MAC or Multiply
ReLu
Add
Divide
Exponent
Compare
Data
to
Mgr
Data
from
Mgr
Notes: StreamingOps
MAC, Multiply
SIMD Wrapper
add/divide/exponent/compare

## Slide 42: Processing (PE) Layer
Streaming operations operate directly on data
SIMD Wrapper performs post stOp tasks
Notes: StreamingOps
MAC, Multiply
SIMD Wrapper
add/divide/exponent/compare

## Slide 43: Detailed Block Diagram
Manager
PE
D
R
A
M

## Slide 44: Detailed Block Diagram

## Slide 45: Test Performance
Tested against multiple fan-ins
[27]
[27]

## Slide 46: Baseline ANN Performance

## Slide 47: AREA
Area based on DiRAM4
  SSC needs to fit into footprint of DiRAM4 sub-memory
  available area is 2.43 sq-mm

## Slide 48: Power/Area Scaling assumptions
Scaling based on synthesizing representative block at 28nm and 65nm
  Designed using 65nm library, 28nm is target technology
Area
Power

## Slide 49: Manager AREA
Utilization
Blocks

## Slide 50: PE AREA
Utilization
Blocks

## Slide 51: Area placement study
Placed and routed without DRC or LVS
Routing congestion showed minimal hotspots
Parasitics used in Primetime for power analysis

## Slide 52: Power Summary
Power estimates based on CONV-294 testcase simulation
  back to back operations
  accumulate DRAM access and use DiRAM4 datasheet [14]
  TSV capacitance from [4]
  parasitics from layout
  designed using 65nm library
  28nm is target technology
  power and area scaling based on synthesizing representative blocks
Notes: back to back operations
accumulate DRAM access and use DiRAM4 datasheet
TSV energy from

## Slide 53: Comparison
Best comparison is to NeuroStream and DaDianNao
  Scaled
  Goldilocks ratio

## Slide 54: Summary
Real world applications will require multiple artificial neural networks
  current solutions consume significant power and real-estate
A 3DIC solution that includes:
  A proposed custom 3D-DRAM
  Instructions and data structures
  Purpose designed functions to accelerate a Artificial Neural Networks
  Architecture to take advantage of 3D technology
Overall area and power improvement
Notes: That concludes my presentation.
Thank you

## Slide 55: Publication(s)
Multi-ANN Edge System based on a Custom 3DIC DRAM - submitted to IEEE journal on emerging technologies and selected topics
Using a 2-D Laser Scanner along with Cogent Confabulation as a Localized Navigation Aid - still trying to find an appropriate journal

## Slide 56: References

## Slide 57: References

## Slide 58: Backup

## Slide 59: Discrimination
Complex
Linear

## Slide 60: Artificial Neural Networks Rate-based
Information stored in connection weights
Output of network is class probability or a value
Output of neuron is fixed value
Multiple layers of neurons
Outputs of each layer feeds next layer
Notes: Keep concise
Mention ReLu function

## Slide 61: Manager Layer
Decodes instructions
  sub-descriptors are sent to dependent blocks
Reads and writes to main memory
Communicates to host and other SSCs
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 62: Feature kernels

## Slide 63: Processing (PE) Layer
Streaming operations operate on data directly from the Stack bus
  MAC, Multiply
SIMD Wrapper performs post stOp tasks
  add/divide/exponent, sends result back to manager
Notes: StreamingOps can also designed to operate on data from registers (or small local memory)
  many ANN’s share a common kernel (CNNs) or operate on same input ROI
  in some cases, storing the kernel or ROI in local memory may avoid unnecessary DRAM reads and IO energy
  first convolution could be performed on kernel streamed from DRAM and further convolutions use local memory for one of the arguments
    on PE the objective will be to maintain low ratio of local memory to processing
  May consider small cache on Controller layer although this will still consume Stack bus TSV power

## Slide 64: Power/Area Scaling assumptions
Scaling based on synthesizing representative block at 28nm and 65nm
  designed using 65nm library
  28nm is target technology

## Slide 65: DRAM and Stack Buses

## Slide 66: Manager Controller

## Slide 67: MRC

## Slide 68: RDP

## Slide 69: MWC

## Slide 70: PE Controller

## Slide 71: SIMD Wrapper

## Slide 72: Streaming Operations

## Slide 73: Classifier Implementation
Separate into sub-layers

## Slide 74: Classifier Implementation
Additional processing absorbed by layer l ANe MAC operation

## Slide 75: Pooling Implementation
Pooling performed by ordering previous layers calculation

## Slide 76: Example DRAM Access Sequence

## Slide 77: Example Image Recognition CNN
Example taken from Krizhevsky, Sutsever, Hinton 2012 [Kri12]
Seven layers but only first 3 layers shown
~60M parameters(~2Gb), ~2GFLOP

## Slide 78: TSV Power
from [Liu12]

## Slide 79: DiRAM4 Stack
from [Pat14]

## Slide 80: FMA Power/Area Estimate
Consider an FMA running at the Stack bus speed of ~1GHz, from [GH11] table 1

## Slide 81: FMA Power/Area Estimate
From [GH11] figure 10 scaling from 45nm to 32nm whilst maintaining the mm2/Gflop suggests a scaling factor of 0.53

## Slide 82: TSV Area
Power Delivery
  ~2000TSV’s ~0.1mm2
Stack Bus
  2737 signals
  Assume 2:1 for GND/VCC ~ 5500 TSV’s
  5um pitch ~ 0.14mm2/PE
  8.8mm2 for 64 PE’s
DRAM Bus
  4255 signals ~ 8500 TSV’s
  13.6mm2 for 64 Ports

## Slide 83: State of the Art Older ASIC’s
NeuroCube1
  uses HMC 3D-DRAM but dependence on SRAM limits support to CNNs
Eyeriss2
  discusses DRAM accesses but their focus is on the convolution operation
  supports CNN convolution operation only
NnSP3
  uses cache between DRAM and 8Mb SRAM and will be limited by DRAM bandwidth
  does not discuss multi-devices
Neuflow4
  limits their support to CNNs and in the case of Eyeriss only supports the convolution
  will not support locally-connected ANNs
Notes: What measure would you use?

## Slide 84: State of the Art GPU’s
GPU’s target the general market and employ infrastructures not necessary for NN implementation
  we associate power of GPU solution ~100-200W
  Will still be limited by memory bandwidth although they are starting to utilize 3D-DRAM
  general purpose architecture makes it hard/impossible to make full use of theoretical performance
[Far11]

## Slide 85: Detailed Block Diagram